## Slide 1: Supply Voltage Biasing in Synopsys
Andy Whetzel
University of Virginia

## Slide 2: Agenda
Quick Background
  FinFET technology
Motivation
Supply-Biased Design
Proof-of-Concept Results
Challenge in Synopsys
Proposed Flow
Tools
  Custom Designer
  SiliconSmart
  Milkyway
  Library Compiler
Progress & Future Work

## Slide 3: Background
FinFET Technology
Scalable
Higher drive strength per unit silicon
Image from: http://www.ece.uc.edu/~kroenker/Research/Research%20Project%20Summaries/FINFET_image004.jpg
Image from: http://www.siliconsemiconductor.net/images/news/image-76523-2012-12-12.jpg

## Slide 4: Motivation
Body biasing does not work on FinFETs
MOSFET vs. FinFET:
https://www.semiwiki.com/forum/content/attachments/5665d1355855218-planar-vs.-3d-finfet.jpg
Notes: FinFETs resistant to body effects

## Slide 5: Supply Biased Inverter Gate

## Slide 6: Ring Oscillator
11 Inverters
Swept bias voltage from -0.1 V to 0.1 V
  1.1 V nominal
Measured frequency, active power, and static power vs. bias voltage

## Slide 7: Ring Oscillator Results
Chart: Normalized Frequency vs. Bias
| -0.1 | -0.09 | -0.08 | -7.0000000000000007E-2 | -0.06 | -0.05 | -3.9999999999999897E-2 | -2.9999999999999898E-2 | -1.99999999999999E-2 | -9.99999999999991E-3 | 0 | 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 7.0000000000000007E-2 | 0.08 | 0.09 | 0.1
 | 0.72612 | 0.75745 | 0.78831 | 0.81847 | 0.8478 | 0.87607 | 0.90329 | 0.92944 | 0.95429 | 0.97785 | 1 | 1.0209 | 1.0401 | 1.0577 | 1.0737 | 1.088 | 1.1005 | 1.1112 | 1.12 | 1.1271
Chart: Active Power vs. Supply Bias
| -0.1 | -0.09 | -0.08 | -7.0000000000000007E-2 | -0.06 | -0.05 | -3.9999999999999897E-2 | -2.9999999999999898E-2 | -1.99999999999999E-2 | -9.99999999999991E-3 | 0 | 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 7.0000000000000007E-2 | 0.08 | 0.09 | 0.1
 | 0.63392 | 0.66553 | 0.69799 | 0.73174 | 0.76677 | 0.80222 | 0.83981 | 0.87783 | 0.91713 | 0.95814 | 1 | 1.044 | 1.0893 | 1.1375 | 1.1875 | 1.2409 | 1.2986 | 1.3622 | 1.4331 | 1.5139 | 1.6087
Chart: Static Power vs. Supply Bias
| -0.1 | -0.09 | -0.08 | -7.0000000000000007E-2 | -0.06 | -0.05 | -3.9999999999999897E-2 | -2.9999999999999898E-2 | -1.99999999999999E-2 | -9.99999999999991E-3 | 0 | 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 7.0000000000000007E-2 | 0.08 | 0.09 | 0.1
 | 1.2036 | 1.041 | 0.9163 | 0.82183 | 0.75281 | 0.70718 | 0.68493 | 0.69021 | 0.73148 | 0.82527 | 1 | 1.302 | 1.8058 | 2.6278 | 3.9509 | 6.0491 | 9.3304 | 14.4004 | 22.1119 | 33.662 | 50.5847

## Slide 8: Problem with Synopsys
Synopsys cannot correctly connect supply-biased gates (high output to NMOS, low output to PMOS).
Characterizing the gates is difficult because many vectors are not possible.
These gates can be viewed as similar to differential signaling.
  We have found that Synopsys does not readily support this.

## Slide 9: Proposed Flow
1. Create Schematics and Layout of Standard Cells and Supply-Biased Cells in Custom Designer
2. Characterize Standard Cells using Synopsys SiliconSmart
3. Convert Output of SiliconSmart to Binary using Library Compiler
4. Synthesize Block in Design Compiler using Standard Cell (Non-Biased) Library
6. Manipulate Netlist Generated from Design Compiler to Implement Supply-Biased Cells in ICC
5. Export Layout from Custom Designer and Import into Milkyway Environment

## Slide 10: Custom Designer
Standard Schematic and Layout Editing
Netlist from Schematic
GDS, LEF, DEF, etc. from Layout View

## Slide 11: SiliconSmart
Inputs to SiliconSmart (when starting from scratch):
  Spice netlist
  Instance files with ports and cell function
    Sometimes SiliconSmart can recognize a cell’s function from its netlist, but it’s always a good idea to ensure that it is correct.
  Configure.tcl file, which includes:
    Operating conditions
    Model names and files
    Simulator setup information
Outputs from SiliconSmart:
  Liberty file with timing and power information (.lib format, human readable)

## Slide 12: Library Compiler
Should be extension of SiliconSmart in my opinion
Converts .lib files to .db (binary) which can be read and used by Synopsys tools
  We use these .db files for Design Compiler and ICC in this flow

## Slide 13: Milkyway Environment
Import LEF file from Custom Designer for both the standard “reference” library and supply-biased library
  This creates CEL and FRAM views for use in ICC

## Slide 14: Tool-Specific Challenges
SiliconSmart:
  It is difficult to define a supply-biased cell’s function because the inputs and outputs have different logic high and low values. Many vectors are disallowed (different logic values of high and low input) but SiliconSmart will still test these vectors unless told not to.
  We have two supplies from which to measure leakage and switching power for each input.
  Characterizing sequential cells is difficult because of timing issues.
Design Compiler
  Will not recognize “high” and “low” (shifted up and shifted down) inputs and outputs.
  Does not support differential signaling.
IC Compiler
  We now need power straps for 4 supplies
  Arranging layouts is more challenging

## Slide 15: Progress
Schematics and layout complete in Custom Designer.
Standard non-biased cells are characterized.
CEL and FRAM view of both biased and non-biased cells.
  Seems to be some trouble with pin extraction, ICC won’t recognize pins
Synthesized FFT in Design Compiler using non-biased cells.

## Slide 16: Future Work
Characterize supply-biased cells.
Figure out how to extract pin information correctly.
Optimized layout for supply-biased cells.
Characterize supply-biased cells under 3 conditions: no bias, forward bias, and reverse bias.
Adjust netlist to use supply-biased cells, complete layout of supply-biased FFT.

## Slide 17: Questions?